## Slide 1
Research Objectives
Development of an efficient two-dimensional CFD model for simulating planar, anode-supported SOFCs operated with methane gas (internal reforming is considered)
  FLUENT is used as a numerical platform for conservation and transport calculation
  Charge transport and electrochemical reaction in the active reaction layers are accurately considered by the electrochemical effectiveness model
  Validation of model by comparison with previous micro/macroscale model results
 Objectives
Contact information
* Corresponding author. jinhnam@gmail.com (J.H. Nam).
Conclusion
A two-dimensional CFD model for planar, anode-supported, methane-fueled SOFCs is developed and validated
Electrochemical effectiveness model is utilized to accurately predict the current generation rate in the active reaction layers with less computational costs
The proposed numerical approach enables the efficient consideration of electrode microstructural effects in CFD calculation platform
Computational Model
Effectiveness Model
Numerical Model
 Anode-supported SOFCs
A five-layer PEN structure with straight gas channels and interconnect layers
 Model Configuration
Various sub-models are incorporated into FLUENT platform utilizing the user-defined function, scalar, and memory (UDF, UDS, UDM) capabilities
A computational Fluid Dynamics Model development for SOFCs with Direct Internal Reforming base on Electrochemical Effectiveness Concept
A. Jeong1 , J. H. Nam2*, C.J. Kim1
1School of Mechanical & Aerospace Engineering, Seoul National University, KOREA
2School of Mechanical Engineering, Daegu University, KOREA
Results and Discussion
 Current-Voltage Performance
 Temperature Distribution (K)
 Species Mole Fraction in Anode
Effectiveness factor is composed of the base effectiveness and the relative effectiveness
Using effectiveness model, significant calculation cost is saved w/o accuracy loss
React. I (SR, steam reforming):
React. II (WGS, water-gas shift):
React. III (RM, reverse methanation):
Cell length = 10 cm
CINT (cathode interconnect layer) 0.5 mm
CGC (cathode gas channel) 1 mm
CCCL (cathode current collector) 50 m
CFL (cathode functional layer) 20 m
ELEC (electrolyte) 10 m
AFL (anode functional layer) 20 m
ASL (anode substrate layer) 1 mm
AGC (anode gas channel) 1 mm
AINT (anode interconnect layer) 0.5 mm
eff = Effectiveness factor
Only one cell is placed in AFL or CFL (in thickness)
Correlation eq.
Reforming reaction
Global three-step reforming is assumed to occur inside ASL
Intrinsic reaction kinetics proposed by Xu and Froment (1989) is used
 | Anode side | Cathode side
Inlet species | H2, H2O, CH4, CO, CO2 | O2, N2
Inlet temperature, T∞ (°C) | 800 | 800
Steam-to-carbon ratio, SC | 2.5 | 2.5
Pressure, pt,∞ (bar) | 1 | 1
Limit current density (A/cm2) | 1.0 | 4.0
Simulated Operating Condition
Good agreement is found between the present CFD model and the previous micro/macroscale model
Counter-flow case shows better performance than co-flow case primarily because of higher temperature (higher reaction rate)
Shin and Nam, 2015, Electrochim. Acta
Xu and Froment, 1989, AIChE J.
Sohn et al., 2016, Int. J. Hydrogen Energy
Air Channel
Fuel Channel
Anode
Air Channel
Fuel Channel
Anode
Counter-flow configuration @ Vcell = 0.780 V & icell = ~0.65 A/cm2
Co-flow configuration @ Vcell = 0.745 V & icell = ~0.65 A/cm2
Standard condition
~65% Fuel Utilization
(0.65 A/cm2)
Mole fraction of CH4
Anode
Fuel Channel
Anode
Fuel Channel
Anode
Fuel Channel
Anode
Fuel Channel
Anode
Fuel Channel
Anode
Fuel Channel
Co-flow
Counter-
Co-flow
Counter-
Mole fraction of H2O
Mole fraction of H2
Co-flow
Counter-
In co-flow case, temperature gradually increases along the flow direction; the lowest temperature appears near the inlet due to active reforming reaction
In counter-flow case, the maximum temperature appears in between the inlet and outlet; temperature is lower near the fuel inlet due to reforming reaction and is lowest near the air inlet due to cooling
Mole fraction of CH4 shows that reforming reaction is completed near fuel inlet; counter-flow case has shorter reaction zone due to higher temperature
Mole fraction of H2O decreases due to reforming reaction and increase due to electrochemical reaction (mole fraction of H2 shows opposite behaviors)
0.745 V
0.679 A/cm2
0.780 V
0.666 A/cm2
Total 9000 cells is used in FLUENT