## Slide 1
Lattice Boltzmann Simulation of Water Transport in Gas Diffusion Layers of PEMFCs with Different Inlet Conditions
Research Background & Objectives
Theory & Calculation
Seung Hun Lee1, Jin Hyun Nam2,*, Hyung Min Kim3, Charn-Jung Kim1
1School of Mechanical & Aerospace Engineering, Seoul National University
2School of Mechanical Engineering, Deagu University
3Department of Mechanical System Engineering, Kyonggi University
Fig. 1 Two-dimension nine-velocity
(D2Q9) model
Fig. 2 The numerical flowchart of
lattice Boltzmann method
e
ˆ
0
e
ˆ
1
e
ˆ
2
e
ˆ
3
e
ˆ
4
e
ˆ
5
e
ˆ
6
e
ˆ
7
e
ˆ
8
 Research Background
Interface condition at the inlet boundary of the gas diffusion layers (GDLs) is an important factor for liquid water transport therein
  Liquid water saturation level inside GDL is significantly affected by how water is introduced into GDL from CL or MPL
  Two ideal inlet boundary conditions are generally considered (uniform pressure BC (UPBC) and uniform flux BC (UFBC)
 Objectives
Multi-phase(*) lattice Boltzmann method (LBM) is adopted to study the dynamic transport behaviors of liquid water in GDLs
The effects of different inlet boundary conditions on the liquid water transport and saturation level are investigated
 Liquid Water Saturation in GDL
In UPBC case, the saturation profile shows lowest saturation level and the time for reaching the steady state is fastest
The saturation difference is clearly observed between case (b) and (c)
  The average saturation level increases as the number of separate liquid water reservoirs increases
  In UPBC case, the number of inlet reservoirs is a more important factor that governs the liquid water saturation level in GDL than the size of the reservoirs
Conclusion
We carried out two-phase LB simulations for the liquid water transport in GDLs of PEMFCs with different inlet boundary conditions
  The result indicates that the number of reservoirs at the inlet boundary of GDL significantly influences the liquid water saturation level
  Minimizing the number of inlet reservoirs can reduce the liquid water saturation level and thus enhance gas diffusion in GDL
Results and Discussion
 Snapshots from LB Simulations
As the number of liquid water reservoir increases, more paths are formed for liquid water transport in GDL
  At the earlier times, liquid water transport behavior is observed to be similar in all cases; however, the difference becomes more conspicuous as the flow time progresses
  Similar characteristics of liquid water are shown in case (a) and (b) for small numbers of larger reservoirs vs. case (c) and (d) larger numbers of smaller reservoirs
  In sufficiently fewer reservoirs, liquid water tends to concentrate around a single transport path that is easier to flow through, which is comparable to the UPBC result
Contact information
* Corresponding author. jhnam@daegu.ac.kr (J.H. Nam).
(*) Liquid water and air is treated as two different components, and
water condensation/evaporation is not considered
 Lattice Boltzmann Method (LBM)
Derived from gas kinetic theory, the Motion of molecules are expressed by distribution function
By adopting BGK (Bhatnagar-Gross-Krook) model for collision terms, LB equation is expressed in terms of discrete particle distribution
Here, is relaxation time and is equilibrium distribution and is lattice velocity in each direction
By applying D2Q9 model (Fig. 1), the discretized LB equation is expressed as
Iteration
loop
Initialize
from initial condition
Streaming step :
Collision step :
Apply boundary condition and compute
The equilibrium distribution is derived from Maxwell-Boltzmann distribution function as
Where the density, velocity, and weighting factors are calculated as
Shan-Chen Model for multi-phase interaction
  Fluid-fluid interaction:
  Fluid-solid adhesion:
  Interaction potential:
Shan & Chen, 1993, Phys. Rev. E
 Inlet Condition for Liquid Water entering GDL
The total domain size is 1000600 lu (1000600 m) with GDL region of 1000250 lu (1000250 m)
  Uniformly hydrophobic circular inclusions are formed in the GDL region to model porous structure (contact angle = 110, porosity = 0.72)
  Uniform pressure BC (UPBC) is implemented by placing a single reservoir (height 10 lu) under the GDL domain
Uniform flux BC (UFBC) is implemented by placing many small reservoirs (50% of inlet surface) segmented by solid walls
  For regular cases, the reservoir size is uniform (regular case), and for random cases, the size is randomly chosen 20-100lu
  Inlet velocity is set to a sufficient low value to ensure that capillary-driven liquid water transport occurs in the model GDL structure
Fig. 3 Schematic GDL structure with different inlet conditions:
(a) UPBC (b) UFBC (c) randomly distributed BC
Fig. 4 Liquid water distribution with different inlet conditions
(b) 5 reservoirs (regular size and location)
(c) 10 reservoirs (regular size and location)
(d) Random reservoirs (12 reservoirs , random size and location )
(a) Uniform pressure
Fig. 5 Liquid water saturation profile of (a) UPBC, (b) 5 reservoirs, (c) 10 reservoirs, (d) randomly distributed reservoirs, (e) average saturation
(a)
(b)
(c)
(e)
(d)