## Slide 1
Two-dimensional Lattice Boltzmann Simulation of Liquid Water Transport
in Gas Diffusion Layers of PEMFCs
Research Background & Objectives
Theory & Calculation
Seung Hun Lee1, Jung Ho Kang2, Jin Hyun Nam3,*, Hyung Min Kim4
1School of Mechanical & Aerospace Engineering, Seoul National University
2Air Conditioning and Energy Solution R&D Group, LG Electronics
3School of Mechanical Engineering, Daegu University
4Department of Mechanical System Engineering, Kyonggi University
Fig. 1 Two-dimension nine-velocity
(D2Q9) model
Fig. 2 The numerical flowchart of
lattice Boltzmann method
e
ˆ
0
e
ˆ
1
e
ˆ
2
e
ˆ
3
e
ˆ
4
e
ˆ
5
e
ˆ
6
e
ˆ
7
e
ˆ
8
 Research Background
Liquid water transport in gas diffusion layers (GDLs) of PEMFCs
  GDL wettability is a critical factor for cell performance by influencing the liquid water content inside the PEMFC
  Hydrophobic PTFE coating is commonly used to facilitate the liquid water drainage from GDLs
 Objectives
Multi-phase(*) lattice Boltzmann method (LBM) is adopted to study the dynamic transport behaviors of liquid water in mixed-wettability GDLs
The effects of hydrophobic/hydrophilic particle proportion on the liquid water transport and saturation level are investigated
 Liquid Water Saturation in GDL
The saturation difference is more noticeable above 150 μm thickness of GDL
  The saturation profile is higher in uniformly hydrophobic case than mixed-wettability case
  The time for reaching the steady state is slightly faster in the mixed-wettability case
  The average saturation level increases as the portion of PTFE-coated carbon fibers increases from 50% to 100%
There seem to be an optimal portion of PTFE-coated carbon fibers which minimize the saturation level in GDL
Conclusion
We conducted LBM simulation for two-phase transport of liquid water in mixed-wettability and uniformly hydrophobic GDLs of PEMFCs
  The result indicates that the mixed-wettability GDLs can reduce the liquid water saturation level and thus enhance gas diffusion in GDL
  LBM is believed to be a proper analysis method for simulating microscale, two-phase, capillary-driven liquid water transport in porous GDLs
Fig. 5 Liquid water saturation profile of (a) mixed-wettability (50% PTFE-coated), (b) uniformly hydrophobic (100% PTFE-coated), (c) average saturation
Results and Discussion
 Snapshots from LB Simulations
Fig. 4 Liquid water distribution with mixed-wettability: 80° (gray) vs. 110° (white) is (a) 50% PTFE-coated, (b) 100% PTFE-coated
As the portion of hydrophobic carbon fibers (PTFE-coated) increases, more paths are required for liquid water transport in GDL
  Only one breakthrough is observed in mixed-wettability case vs. uniformly hydrophobic case
  Mixed-wettability seems to facilitate the formation of preferential paths for liquid water transport by reducing capillary entry pressure, which in turn reduces liquid water saturation
  In mixed-wettability GDL, liquid water tends to concentrate around a single transport path that is easier to flow through
(b)
(a)
(c)
Contact information
* Corresponding author. jhnam@daegu.ac.kr (J.H. Nam).
(*) Liquid water and air is treated as two different components, and
water condensation/evaporation is not considered
 Lattice Boltzmann Method (LBM)
Derived from gas kinetic theory, the Motion of molecules are expressed by distribution function
By adopting BGK (Bhatnagar-Gross-Krook) model for collision terms, LB equation is expressed in terms of discrete particle distribution
Here, is relaxation time and is equilibrium distribution and is lattice velocity in each direction
By applying D2Q9 model (Fig. 1), the discretized LB equation is expressed as
Iteration
loop
Initialize
from initial condition
Streaming step :
Collision step :
Apply boundary condition and compute
The equilibrium distribution is derived from Maxwell-Boltzmann distribution function as
Where the density, velocity, and weighting factors are calculated as
Shan-Chen Model for multi-phase interaction
  Fluid-fluid interaction:
  Fluid-solid adhesion:
  Interaction potential:
Shan & Chen, 1993, Phys. Rev. E
 Model GDL Structure
2D random structure
  Total: 1000500 lu (1000500 m)
  GDL: 1000250 lu (1000250 m)
  Porosity of GDL ~ 0.72
  Circular particles are randomly generated in the domain, by varying radius (6~9 μm) and position
  Particle wettability is also randomly assigned according to given proportion
Fig. 3 Generated GDL structure with mixed-wettability (contact angle: red=80°, blue=110°)
 Inlet Condition for Liquid Water entering GDL
Inlet condition is known to be an important factor that alters the liquid water distribution inside GDLs
There are generally two broad categories: Uniform flux BC (UFBC) and uniform pressure BC (UPBC)
We adopted the UPBC by placing 10-lu (10-m) height void space just under the GDL domain
  Inlet velocity is set to a sufficient low value to ensure that capillary-driven liquid water transport occurs in the model GDL structure