## Slide 1
Research Objectives
Electro chemical effectiveness model can be properly incorporated with CFD simulation codes, reducing computational costs allowing the consideration of microstructural effects
  Too many grid points are required for conventional microscale model to capture the reaction/transport process in mixed ionic-electronic conducting (MIEC) electrodes
Micro/CFD model is developed using FLUENT and the effectiveness model with the user-defined function (UDF) and user-defined memory (UDM) capabilities
 Objectives
Contact information
* Corresponding author. jinhnam@gmail.com (J.H. Nam).
Conclusion
Micro/CFD model is developed based on the electrochemical effectiveness model using FLUENT (UDF, UDS, and UDM)
The reliability of the micro/CFD model is validated by the excellent agreements in the I-V curve and the variation of temperature and current density with the previous microscale model results
The effects of interconnect thermal conductivity are investigated using the model
Grid structure and Calculation algorithm
 Grid structure
Electrochemical Effectiveness Model
Fig. 1 Relative effectiveness factors:
Data and correlation curves
 Effectiveness model definition
An efficient and accurate method to determine the current generation in thin active reaction layers
Total current generated in active react. layer
Effectiveness factor
decomposition
Thiele modulus
Base effectiveness at zero overpotential
Relative effectiveness at finite overpotential
Dimensionless overpotential
 Relative effectiveness
The relative effectiveness decreases from 1.0 towards 0.0 with overpotential
For T>3, the relative effectiveness converges into a single functional curve
A simple correlation equation is devised to retrieve the relative effectiveness
Micro/CFD model development for solid oxide fuel cells based on electrochemical effectiveness model
Areum Jeong1 , Jaeyeung Song1 , Jin Hyun Nam2*, Charn-Jung Kim1
1School of Mechanical & Aerospace Engineering, Seoul National University, KOREA
2School of Mechanical Engineering, Daegu University, KOREA
Validation with Microscale Model & Results
 Current - voltage curve
 Temperature distribution (K)
 Variables of along the axial coordinate
Fig. 2 (a) Electrochemical reaction/ charge transport process (b) Grid number in y-direction
Fig. 2 (c) Simplified mesh grid in x-direction
2-dimensional grid structure
CINT : Cathode interconnect
CCH : Cathode Channel ( Air Channel )
CCH_C : Cathode Channel Contact layer
dCFL : Cathode Functional Layer ( Non-active )
aCFL : Cathode Functional Layer ( Active )
ASL : Anode Substructure Layer
dAFL : Anode Functional Layer ( Non-active )
aAFL : Anode Functional Layer ( Active )
ACH_C : Anode Channel Contact Layer
ACH : Anode Channel ( Fuel Channel )
AINT : Anode Interconnect
 Calculation algorithm (FLUENT solver user access)
Fig. 4 Current-voltage curves for an IT-SOFC operating at 700°C
Fig. 3 Calculation Algorithm
 Species concentration (Mol/m3)
Fig. 5 Variation of variables along the axial coordinate in an IT-SOFC operating at 700°C
Counter-flow
Fig.6 (a) Temperature distribution in an IT-SOFC operating at 700°C
Co-flow
Co-flow
Counter-flow
Counter-flow
 Effect of thermal conductivity at interconnect (@ 0.7 Vcell)
Temperature Distribution (K)
Co-flow
Counter-flow 0.7
Species concentration (Mol/m3)
Co-flow
Counter-flow
Fig.6 (b) Temperature distribution in an IT-SOFC operating at 700°C
Fig.7 (a) Species concentration in an IT-SOFC operating at 700°C
Fig.7 (b) Species concentration in an IT-SOFC operating at 700°C
Thermal conductivity | Co-flow |  | Counter-flow | 
5 W/m-K | 0.870 A/cm2 | 1259.20 K | 0.920 A/cm2 | 1307.33 K
25 W/m-K | 0.902 A/cm2 | 1258.95 K | 0.952 A/cm2 | 1299.81 K
125 W/m-K | 0.930 A/cm2 | 1242.59 K | 0.965 A/cm2 | 1281.54 K
Current density according to thermal conductivity at interconnect
Fig.8 (a) Temperature distribution in an IT-SOFC operating at 700°C
Fig.8 (b) Temperature distribution in an IT-SOFC operating at 700°C
Fig.9 (a) Species concentration in an IT-SOFC operating at 700°C
Fig.9 (b) Species concentration in an IT-SOFC operating at 700°C